## Slide 1: NB-IoT
Introducción

## Slide 2: Overview
NB-IoT is a cellular low power wide area technology introduced in the 3GPP. It is expected to ease the massive deployment of the IoT. LTE Cat-NB1 (NB-IoT) operates at a minimum system bandwith of 180Khz for both directions. It is possible for a GSM operator to replace one GSM carrier of 200 KHz with an NB-IoT app. (1)
The NB-IoT air interface is well optimized to ensure harmonious coexistence with LTE, which means, when an NB-IoT is deployed inside an LTE carrier, the performance of LTE or Cat-NB1 cannot be compromised. Thus, NB-IoT enables flexible deployment of Massive IoT to network providers as:
In band: Integrated as part of the resource regularly used for tge eNB communication.
Guard Band: Uses the freq band of 180 KHz (between the last PRB and the channelization edge).
Standalone system: based on a re-farmed channel of a legacy GSM/GPRS system operated by a service operator.

## Slide 3: NB-IoT system Design
NB-IoT will be introduced with the following design targets for all operations:
Improved indoor coverage: Achieve and extended coverage of 20 dB compared to legacy GPRS devices. Achieving a 164 dB max. coupling loss, supporting 160 bps of data rate.
Massive number of low-throughput devices: It is targeted at least 52547 devices (40 devices per househould).
Reduced complexity and Improved Power efficiency.
Latency: 10 sec or less of latency.

## Slide 4: NB-IoT Features
NB-IoT can support more than 52K connections per channel. Due to small data transfers at low frequency.
NB-IoT uses a BW of 180 KHz and operates in HD-FDD (half duplex operation).
NB-IoT is designed due to provide prolonged battery life.
NB-IoT 20 db coverage in noise interference.
NB-IoT offers operating mode flexibility (LTE and 2G together).
NB-IoT doesn’t support higher modulation scheme than QPSK.
NB-IoT Low-Data-Rate apps (which the requirement for high capacity flash memory reduce the chip area and the cost of devices).
NB-IoT operates in Licensed Band and provide (if wished) telecom. Lvl of security.
NB-IoT achieved signaling optimization.

## Slide 5: CASE STUDY: ENERGY EFFICIENT HEALTH MONITORING SYSTEM FOR GREEN COMMUNICATION
Conclusions:
NB-IoT provide a cost effective, reliable, and low power solution. It can coexist with the existing LTE celular networks, therefore no new infraestructure is required, so the installation cost is also low.